Rainbow Security Systems.                               Tel  01604  627227

www.rainbowsecuritysystems.co.uk                                                                                                                   Fax 01604  627337

## User Guide For SCANTRONIC 9651 Panel.

### TO FULL SET THE ALARM	Enter User Code, Press A.

TO UNSET THE ALARM	Enter User Code.

IF ALARM ACTIVATES	Enter Code To Silence Alarm.

TO LOCATE REASON OF ACTIVATION	Panel Will Display Area Of Initial Trigger of Alarm, To

View Other Areas Triggered (If Applicable) Press The

“Tick” Key To Accept The “Next” Prompt. Other Areas

Of Alarm Will Appear.

TO CLEAR REASON OF ACTIVATION	Enter Code Only.

TO NIGHT SET THE ALARM	Enter Code, Press B (zones omitted as programmed by Engineer).

TO UNSET NIGHT SET ON ALARM	Enter Code Only.

TO DAY SET FOR PETS		Enter Code, Press C (zones omitted as programmed by Engineer).

TO UNSET DAY SET FOR PETS	Enter Code Only

TO CHANGE MASTER CODE	Key in the master user code, Press 4.

(note: only the master user can                          (the display prompts for the code that you wish to change)

change this)                                                         Enter the existing master user code and press tick.		(the display will show UO1:User 1) press tick.

Enter your new user code, which will be displayed, on screen.	Ensure that this code is correct and press tick.

SETTING TIME AND DATE                           Key in the master user code, Press 6. (the display shows

(note: only the master user can                           the date). Key in 2 digits for the day followed by “Tick”.

change this)                                                         Key in 2 digits for the month followed  by “Tick”.

Key in 2 digits for the year followed by “Tick”.

(the display shows the time), Key in 2 digits for the hour

Followed by the “Tick” (use the 24hr clock). Key in 2

Digits For the minutes followed by the “Tick”.

(the display will now show  the new time and date).

FAULTS                                                              Should there be a Fault on the system the “(!)” on the

Keypad will Flash or Glow steadily, this may be

Accompanied by an intermittent audible warning.

To determine the cause of the Fault proceed as follows:

Key in the access code

If the “(!)” lamp is flashing or glowing, there are alerts

The system may display the first alert or it may show

How many alerts exist. Press 1 to view the alerts. The

First alert will be displayed. The alert will be proceeded

By either “Active” or “Inactive”, Active represents an

Existing problem, Inactive represents a resolved

Problem. Press, “tick” to view the next alert. Under certain

Circumstances the alarm may request you to “Call Installer”

Should your alarm system display this, the problem can only

Be corrected by an engineer, in this situation you should

Call Rainbow Security Systems on 01604 627227.

Once you have viewed all the alerts and providing no

Installer Action is required the system will revert to

Displaying the time and date, you may now use the alarm

System as normal.

PANIC BUTTON SET OFF	If pressed. Silence the alarm by entering your code on the

Keypad. Insert the key into the Panic Button and turn it

Clockwise. This will reset the panic button and change the

Colour of the small window from red to green. Now re-enter

Your code into the keypad and press the tick key. The system 	should now be reset.